## Slide 1: Transport Layer
Content: Chapter 6 - Tanenbaum mixed with
Chapter 4 - Kurose
Outline:
Role of Transport Layer
Related Problems and Solutions
TCP/IP Transport protocols

## Slide 2: The Role of the Transport Layer
application
transport
network
data link
physical
logical end-end transport
application
transport
network
data link
physical
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, enhances, network layer services

## Slide 3: Multiplexing/demultiplexing
process
socket
use header info to deliver
received segments to correct
socket
demultiplexing at receiver:
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3

## Slide 4: Sockets
Definition:
A socket is one endpoint of a two-way communication link between two programs running on the network. A socket is bound to a port number so that the transport layer can identify the application that data is destined to be sent to.
An endpoint is a combination of an IP address and a port number. Every TCP connection can be uniquely identified by its two endpoints. That way you can have multiple connections between your host and the server.
Socket API (Application Programming Interface)

## Slide 5: Socket Programming in Python or C
socket( )
bind ( )
listen ( )
accept ( )
recv ( )
send ( )
close ( )
socket( )
connect( )
send ( )
recv ( )
close ( )
S
E
R
V
E
R
C
L
I
E
N
T
Create socket descriptor
Request Connection
Assigns protocol addresses to the socket
Indicates queue size and listening
Wait for connections request
(read)
(write)
Closes socket and finishes connection
Return socket descriptor (s)
binds ip+port to s
(write)
(read)

## Slide 6: Programming Details (1)
Little Endian versus Big Endian: how to store a number in memory:
Little Endian: stores the lowest order bytes first. Used in Intel architecture. Ex: 0x12345678 would be stored as (0x78 0x56 0x34 0x12)
Big Endian: 0x12345678 would be stored as (0x12 0x34 0x56 0x78). Used in RISC architectures. The network format.
Htons: host to network – unsigned short int to Bigendian.
Htonl: host to network – unsigned long int to Bigendian

## Slide 7: Programming Details (2)
struct sockaddr_in channel: data structure to specify a local or remote endpoint address to connect to the socket:
channel.sin_addr.s_addr=htonl(INADDR_ANY)
“This allowed your program to work without knowing the IP address of the machine it was running on, or, in the case of a machine with multiple network interfaces, it allowed your server to receive packets destined to any of the interfaces”.
Defines which version the address family will come from:
Server Address setting
channel.sin_family = AF_INET Address Family for Internet Sockets is IPv4

## Slide 8: Requests server file : client <url> <file> >f
Client (1)

## Slide 9
9
Client (2)

## Slide 10
10
Client (3)

## Slide 11
11
Server (1)

## Slide 12
12
Server (2)

## Slide 13
13
Server (3)

## Slide 14: Transport Layer
Outline:
Role of Transport Layer
Related Problems and Solutions:
  Problem 1: Reliability vs Urgency
  Problem 2: How to address ?
  Problem 3: How to treat losses ?
  Problem 4: How to treat congestion?
TCP/IP Transport protocols

## Slide 15: Problem 1: Reliability vs Urgency
Two types of service:
Connectionless - UDP:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Connection-oriented - TCP:
  handshaking - exchange of control msgs. Phases:
  Connect -> Transfer -> Disconnect.
A segment is a message handled by the transport entities.

## Slide 16: Problem 2: How to Address ?
TCP/IP – transport address => port number
A process should know which port is related with a service:
Extracted from /etc/services:
daytime 13/udp
ftp 21/tcp
telnet 23/tcp
smtp 25/tcp mail
IANA – Internet Assigned Numbers Authority globally coordinates DNS Root, IP addressing, and other Internet protocol resources.

## Slide 17: IANA Internet Assigned Numbers Authority
(http://www.iana.org/assignments/service-names-port-numbers/service-names-port-numbers.xhtml)
“ The port numbers are divided into three ranges:
  System Ports (Well Known): from 0 through 1023.
  User Ports (Registered ): from 1024 through 49151
  Dynamic and/or Private Ports: from 49152 through 65535.
  (Detalhes vide RFC6335)
The System Ports are assigned by the IETF process for standards-track protocols (and on most systems can only be used by system (or root) processes ). The User Ports are assigned by IANA using the “Expert Review” process . Dynamic Ports are not assigned. ”

## Slide 18: Portmapper
How do I request a connection to software that does not use familiar ports? Through the portmapper process:
When creating a service, the application registers itself in the portmapper;
A client requests a known port connection associated with the portmapper (usually port 111); the portmapper returns the port number associated with the desired service;
The user terminates the connection with the portmapper and establishes a new connection with the new address provided.
If an application has high demand, it is better to wait for the connections directly, instead of using the portmapper
  Portmapper is equivalent to phone directory assistance.

## Slide 19: inetd Process Server
19
The portmapper may be associated with a process server - inetd (in the UNIX case).
Do I need a process waiting for connections for each service?
Yes and No. Applications that are not so widely used could be activated on demand: a process server waits for requests and activates the process that can handle them.
If the application has high demand should be waiting for connections directly.
Notes: 19

## Slide 20: Problem 3: How to treat losses ?
3 way handshake in normal scenario
Use Acknowledge. Idea: a CR message to request a connection and ACK message to accept.
Problem: The network may lose, delay, corrupt, or replicate packets (due to retransmissions). The usual cases must be implemented to perform well, but the protocol must deal with unusual cases as well.
The 3-way handshake is the better choice.

## Slide 21: Establishing connections on L4
21
(1) Old duplicate CR
(2) Duplicate CR and ACK
Host 1 realizes that it is duplicate
Host 2 realizes that ACK=z is duplicate
Seq=z, Ack=x
Seq=z, Ack=x
Seq=x, Ack=z
Seq=x
Seq=x
Notes: 21

## Slide 22: Problem of the two Armies
Blue Army Number 1
Blue Army Number 2
White Army

## Slide 23: Closing a connection on L4 (1)
23
Abrupt Closing with Data Loss
Normal case with 3-way Handshake
Notes: 23

## Slide 24: Closing a connection on L4 (2)
24
ACK lost
DR answer Lost
DR answer and DR Lost
Notes: 24

## Slide 25
What is congestion ?
informally: “too many sources sending too much data too fast for network to handle”
different from flow control!
manifestations:
    lost packets (buffer overflow at routers)
    long delays (queueing in router buffers)
a top-10 problem!
25
Problem 4: How to treat congestion?

## Slide 26
(a) Goodput x load (b) Corresponding delay
Although congestion occurs in routers, therefore detected by the network layer, it is caused by traffic sent to the network by the transport layer and therefore is a joint responsibility of these layers.
26
Who cares ?

## Slide 27: Causes/costs of congestion: scenario 1
two senders, two receivers
one router, infinite buffers
output link capacity: R
no retransmission
maximum per-connection throughput: R/2
unlimited shared output link buffers
Host A
original data: lin
Host B
throughput: lout
R/2
R/2
lout
lin
R/2
delay
lin
large delays as arrival rate, lin, approaches capacity

## Slide 28: Causes/costs of congestion: scenario 2
one router, finite buffers
sender retransmission of timed-out packet
  application-layer input = application-layer output: lin = lout
  transport-layer input includes retransmissions : lin lin
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in: original data, plus retransmitted data
‘

## Slide 29: Causes/costs of congestion: scenario 2
idealization: perfect knowledge
sender sends only when router buffers available
finite shared output link buffers
lin : original data
lout
l'in: original data, plus retransmitted data
copy
free buffer space!
R/2
R/2
lout
lin
Host B
A

## Slide 30: Causes/costs of congestion: scenario 2
lin : original data
lout
l'in: original data, plus retransmitted data
copy
no buffer space!
Idealization: known loss packets can be lost, dropped at router due to full buffers
sender only resends if packet known to be lost
A
Host B

## Slide 31: Causes/costs of congestion: scenario 2
lin : original data
lout
l'in: original data, plus retransmitted data
free buffer space!
Idealization: known loss packets can be lost, dropped at router due to full buffers
sender only resends if packet known to be lost
R/2
R/2
lin
lout
when sending at R/2, some packets are retransmissions but asymptotic goodput is still R/2 (why?)
A
Host B

## Slide 32: Causes/costs of congestion: scenario 2
A
lin
lout
l'in
copy
free buffer space!
timeout
R/2
R/2
lin
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
Host B
Realistic: duplicates
packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered

## Slide 33: Causes/costs of congestion: scenario 2
R/2
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
“costs” of congestion:
more work (retrans) for given “goodput”
unneeded retransmissions: link carries multiple copies of pkt
  decreasing goodput
R/2
lin
Realistic: duplicates
packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered

## Slide 34: Causes/costs of congestion: scenario 3
four senders
multihop paths
timeout/retransmit
Q: what happens as lin and lin’ increase ?
finite shared output link buffers
Host A
lout
Host B
Host C
Host D
lin : original data
l'in: original data, plus retransmitted data
A: as red lin’ increases, all arriving blue pkts at upper queue are dropped, blue throughput g 0

## Slide 35: Causes/costs of congestion: scenario 3
another “cost” of congestion:
when packet dropped, any “upstream transmission capacity used for that packet was wasted!
C/2
C/2
lout
lin’

## Slide 36: Congestion Control - Solutions
Where to take action?
Find a good allocation of bandwidth: fair, with good performance, avoiding congestion;
Adjust flow rate;
Consider the particularities of Wireless Networks - although in theory, transport layer is independent of the link layer, in practice, it is necessary to consider the wired and wireless differences.
36

## Slide 37: Desirable Bandwidth allocation
37

## Slide 38: Controlling the Flow Rate (1)
(a) The limit is the small capacity receiver;
(b) The limit is the internal network.
Flow control helps in congestion control

## Slide 39
The criterion for flow rate control has an important effect on performance.
AIMD - Additive Increase Multiplicative Decrease
Controlling the Flow Rate (2)
How much to increase? (TCP has its own algorithm)

## Slide 40
In the Theory: transport protocols are independent of the network and link technologies.
In practice: TCP uses packet loss as a congestion signal, but wireless networks lose packets by error, not congestion. Worse: the nodes move and the quality of the link varies.
Different solutions for different scenarios.
Google has a new algorithm TCP-BBR (Bottleneck Bandwidth and Round-trip propagation time):
https://techcrunch.com/2017/07/20/google-cloud-gets-a-new-networking-algorithm-that-improves-internet-throughput/
40
Particularities of Wireless Networks

## Slide 41: Transport Layer
Outline:
Role of Transport Layer
Related Problems and Solutions:
  Problem 1: Reliability vs Urgency
  Problem 2: How to address ?
  Problem 3: How to treat losses ?
  Problem 4: How to treat congestion?
TCP/IP Transport protocols
  UDP
  TCP

## Slide 42: User Data Protocol - UDP
no connection establishment (which can add delay)
simple: no connection state at sender, receiver. Good for applications with the behavior - request, response - not needing connection establishment overhead. The response is the acknowledgment of the request. If the answer does not arrive, ask again.
small header size
no congestion control: UDP can blast away as fast as desired
why is there a UDP?

## Slide 43: UDP: segment header
43
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
length, in bytes of UDP segment, including header

## Slide 44: RTP – Real-Time Transport Protocol
Several multimedia applications rely on a real-time transport protocol. RTP numbers the packets for the application to decide what to do with packets and losses, but RTP does not retransmit - no time.
It is considered transport protocol implemented in the application layer

## Slide 45: TCP - Transmission Control Protocol Overview RFCs: 793,1122,1323, 2018, 2581
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) inits sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size